## Slide 1: So what does the dataflow of SumCheck look like?
Dataflow

## Slide 2: Example with 1 polynomial in 3 variables
Dataflow

## Slide 3: SumCheck
Claim: “The sum of over all binary inputs is ”
Polynomials Lookup Tables
Dataflow
Notes: In Sumcheck we make a claim that the sum of all binary evaluations of a polynomial is some value H. This seems complicated, BUT, we can leverage a key insight that polynomials in hardware can be stored as lookup tables

## Slide 4: SumCheck
Claim: “The sum of over all binary inputs is ”
0 0 0 | 1
0 0 1 | 2
0 1 0 | 1
0 1 1 | 4
1 0 0 | 3
1 0 1 | 0
1 1 0 | 5
1 1 1 | 8
0 0 0 | 1
0 0 1 | 2
0 1 0 | 1
0 1 1 | 4
1 0 0 | 3
1 0 1 | 0
1 1 0 | 5
1 1 1 | 8
Dataflow
Notes: That means that polynomials look just like this. In this very simple example, we’re just saying that the sum of all values is H = 24

## Slide 5: SumCheck
So can we just sum up the table?
Not exactly.
Multiple rounds → 1 round per variable
Dataflow
Notes: So then, can we just sum up the table? Not exactly. SumCheck is multi-round protocol where we make claims about each variable, for example, x1 x2 and x3 for the polynomial f. Today I will explain the first round; the rest follows recursively

## Slide 6: Round 1 of SumCheck
Key Assumption:
is multilinear
is linear
Claim:
Dataflow
Notes: In round 1, we make a claim about the variable x1, that is, if we sum over all other variables, we get a polynomial of x1. In Hyperplonk, we assume that f is multilinear, or linear in all of the variables. This means that the resuling f1 is also linear, and can be uniquely characterized by 2 points on its line, called evaluations. The claim is now that their sum is H. So how do we obtain these evaluations?

## Slide 7: Round 1 of SumCheck
0 0 0 | 1
0 0 1 | 2
0 1 0 | 1
0 1 1 | 4
1 0 0 | 3
1 0 1 | 0
1 1 0 | 5
1 1 1 | 8
0 0 0 | 1
0 0 1 | 2
0 1 0 | 1
0 1 1 | 4
1 0 0 | 3
1 0 1 | 0
1 1 0 | 5
1 1 1 | 8
Dataflow
Notes: Looking at the table, we first add all terms with x1 = 0

## Slide 8: Round 1 of SumCheck
0 0 0 | 1
0 0 1 | 2
0 1 0 | 1
0 1 1 | 4
1 0 0 | 3
1 0 1 | 0
1 1 0 | 5
1 1 1 | 8
0 0 0 | 1
0 0 1 | 2
0 1 0 | 1
0 1 1 | 4
1 0 0 | 3
1 0 1 | 0
1 1 0 | 5
1 1 1 | 8
Dataflow
Notes: We then add all terms with x1=1. We can easily check that to see that claim was satisifed

## Slide 9: Round 1’s MLE Update
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
---
Set
halve the table,
Go to round 2:
Dataflow
Notes: In order to proceed to round 2, we need to eliminate x1, which is done by fixing x1 to a random value. This results in halving the table size. After this point we repeat for variables x2, x3, etc.

## Slide 10: The same process repeats for round 2. Round 3 is the same but no MLE Update
Dataflow

## Slide 11: Example with 3 polynomials in 2 variables
Dataflow

## Slide 12
Overall Objective
Dataflow

## Slide 13: Example Dataflow
Round 1
Round 2
Dataflow
MLE
Update
The dataflow is the same each rounds, with tables updated and reduced in between rounds.
Notes: SumCheck is actually a multiple round protocol, with 1 round per variable in f. Given the individual tables, in each round i, we solve for a function of variable x_i by summing over the other variables.

## Slide 14
Round 1 Computation
Dataflow
Notes: If we use our example of 4 gates and 2 variables, then the overall objective looks like the equation on the left. round 1 looks like the equation on the right, which involves summing over x2

## Slide 15
is degree 3
4 Coefficients
4 Evaluations
all multilinear polynomials
We want this
Dataflow
Notes: So how we get f1(x1)?
There’s one more property I need to mention: each individual polynomial is multilinear by construction. I won’t go into details here, but the consequence of this is that because of the multiplication term, f1 is a degree 3 polynomial.
Typically, this means we’d need 4 coefficients to describe f1. But we’re going to use evaluations at 4 points instead

## Slide 16
Extensions
Extensions
Linear Extrapolations
Dataflow
Notes: (8:00 mark) So lets look at the dataflow of just the multiply term. Suppose these are the individual tables. First, we will expand the tables to get 4 X1 evaluations for each value of X2. These are called extensions, and they are just linear extrapolations given the multilinearity property

## Slide 17
Extensions
Extensions
Dataflow
Notes: then we compute the products, and then combine like terms. or in other words, sum along the X1 dimension to get the evaluations of f1

## Slide 18: Each table undergoes MLE Update, and then we proceed to round 2, which has the same dataflow as round 1 except no MLE Update.
Dataflow